## Slide 1: Microprocessors I Final Project
By Charlie Shields

## Slide 2: Current Design Analysis
Available:
Arduino UNO
TMP36
LEDs
Data Logger
Battery
Power Switch
Resistors
Obsolete:
Humidity Sensor
Pressure Sensor
Accelerometer

## Slide 3: Humidity & Temperature Sensors
HIH-4030
ASDXACX015PAAA5

## Slide 4: Adafruit MS8607 Breakout
Pressure
Humidity
Temperature
Google:
DigiKey:

## Slide 5: Accelerometer
SparkFun ADXL335 Breakout
SparkFun LIS3DH Breakout

## Slide 7
LD1117V33C
TMP36

## Slide 11: OSH-PARK

## Slide 12
Cost | Phase 1 | Phase 2
Sensors | HIH-4030 ($53k!), ASDX ($35+), ADXL335 ($22.27) | MS8607 ($14.95), LIS3DH ($7.75)
Data logger | $17.50 | $17.50
Total | ~$70+ (with unobtainable parts) | ~$40.20 (all available)
Weight | Phase 1 | Phase 2
Electronics + PCB | ~108-113 g | ~82 g
Battery | ~45 g | ~45 g
Enclosure | ~30-50 g | ~30-50 g
Total | ~138-163 g | ~112-127 g
Power | Phase 1 | Phase 2 (lin reg) | Phase 2 (buck)
Useful load | ~308 mW | ~275 mW | ~275 mW
Regulator loss | ~184 mW (hidden) | ~570 mW | ~50 mW
Total from battery | ~492 mW | ~845 mW | ~325 mW
Est. battery life | ~3 hrs | ~1.5 hrs | ~4-5 hrs
Phase 1 vs. Phase 2

## Slide 13: Improvements
I2C Bus (Heavy)
Linear Voltage Regulator (5.7v drop)